## Slide 1: Adaptive Soft Associative Memory
ECE 560 Project Report
Anand Ramachandran

## Slide 2: Sparse Distributed Memory
n-bit vector space – sparsely populated with random hard addresses
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
Address X
Programming or Reading at X:
Select all addresses within a distance dth of X.
Write X into all locations.
Read and average across all locations.
Memory should not be too sparse. Properties depend on hyper-dimensional vector distribution around a given vector.
Can respond to patterns similar to those stored in memory
Circle of X’ ~ X

## Slide 3
Initially Empty Storage
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
If there is no hard-location near X, create hard-locations in the circle of X mirroring the probability density of SDM
Assumption: The data is very sparse and noisy data is clustered very close to signal.
Thus circles of two different data and associated noise will be disjoint.
Too Much Memory Required: One possible solution

## Slide 4
Address
Data
100101101, 110101001
Initially empty (address, data) pairs. Incoming address and data are both programmed into memory.
Why not always dynamically allocate?
Memory consists of empty address and data locations in the beginning.
User initializes both address and data.
Issue – what if the data is noisy? And the initially programmed address is the noisy?
Other noisy data may not be detected.

## Slide 5: Example
Actual address is 0000
Noisy incoming address is 0001. 0001 stored
Assume memory parameter is dth = 1
Assume address 0010 comes in next
d(0001, 0010) = 2 => 0010 goes undetected
Solution: Adaptively change 0001 to 0000 based on input statistics

## Slide 6: Auto-associative modification
Stored data = Address
Data represented as counters per bit-position
Increment counter at respective bit-position if address has a ‘1’ at that position
Decrement otherwise
-
+
-
+
Data-fields
0 1 0 1
Incoming address
0
1
1
1
soft address

## Slide 7: Adapt the address to data
When a data-field saturates, modify the address bit accordingly
Thus if the first address lodged is noisy, the address will later change to the “signal”

## Slide 8
Address
Data
X
X
X
X
X
X
X
X
‘X’ indicates occupied location
1010
+
-
+
-
0
1
2
3
4
5
6
7
8
9
10
Dynamic Allocation picks the least unoccupied index to program
Automate Dynamic Allocation of memory
Maintain a state of each cell.
Allocate a location if no cell is activated by incoming address based on static priority.

## Slide 9
-40
-39
40
7
Memory Contents
Strength and Unlearning
Define a strength threshold, H
A bit position is strong if the counter at that position has magnitude higher than ‘H’
Memory location is strong if all bit positions are strong
If H = 8, the bit-positions in bold are strong.
Invalidate weak locations when their activation coincides with the activation of another location.
0011 : Strong location 0110 : Weak location
Incoming: 0010
Activates both locations
Weak location will be invalidated, or “unlearned.” Strong location’s contents will be updated and later adapted.

## Slide 10
address
Hamming Distance Unit
Soft Address
Data Management
Data
hit
otherHit
setAddress (dynamic allocation)
adapt
update
strength
rddata
Overall Memory-Cell Architecture
“Learn, Adapt, Unlearn”

## Slide 11: Implementation and Experiments
Implemented in Verilog, parameterized fully
Structural coding can be synthesized.
  Not synthesized.
Memory built to correct erroneous hamming codes
  Symbols: 11111111, 11110000, 11001100, 10101010
  Hamming distance of four between any two codes
  Code can correct 1 bit error per symbol

## Slide 12: Experimental Results
The associative memory can make a successful estimation of the correct symbols from erroneous symbols. After this initial training, it can start correcting 1-bit errors in the code.
Errors are uniform random per bit
Most incoming symbols are erroneous in some experiments

## Slide 13: Thank You! Questions?

## Slide 14: Initial Application studied
Genomic Error Correction.
Ambiguities in portions of a genome due to erroneous duplicates.
Initial project objective: use SDM to filter out statistically more significant genome portions compared to similar statistically less significant genome portions.